## Slide 1
Security-Constrained
Unit Commitment
Salomon Bendayan · MAG Energy Solutions
Python · Pyomo · HiGHS · 24-Bus IEEE Network
June 2026 · Confidential
Notes: Welcome. Today I'll walk through my solution to the three-part SCUC technical test. I'll cover what I built, the key formulation decisions, and why each choice matters for accurate LMP forecasting. Time for questions at the end.

## Slide 2
Why SCUC Matters to a Trading Fund
Day-ahead markets clear via SCUC — the ISO's price-setting engine
LMPs (Locational Marginal Prices) = dual variables of nodal power balance
A more accurate simulator → better LMP forecasts → trading alpha
Three blind spots in the existing simulator needed fixing
Wrong
Startup Costs
No Security
Constraints
No Market
Analysis
Notes: SCUC is what ISO operators run every day to schedule generators. Its outputs — the LMPs — are the prices that electricity traders trade against. If our simulator gets startup costs wrong, or ignores what happens when a line trips, our LMP forecasts will be systematically biased. That bias costs money. These three blind spots are the test.

## Slide 3
Three-Part Test
01
Tiered Startup Costs
Current model: every restart costs the same
Cold boiler restart costs more than hot
Model hot / warm / cold regimes + pre-horizon state
02
N-1 Security Constraints
Current: base-case flows only
Grid must survive any single line outage
Efficiently ensure load is redistributed safely during an outage.
03
Market Analysis
Extract LMPs from dual variables
Merit order, congestion, peak/off-peak
Trader-facing briefing with actionable signals
Notes: The three parts build on each other. Part 1 fixes the economics of the MILP — wrong startup costs lead to wrong unit cycling patterns. Part 2 adds the network security layer that ISOs require. Part 3 extracts market intelligence from the solution. Each part addresses a real limitation.

## Slide 4
Part 1 — The Cold-Start Problem
Unit commitment cycles generators on/off to minimize total cost
Restart cost depends on boiler temperature — which depends on time offline
Flat-cost model underpays for cold restarts → units cycle too much → wrong LMPs
State
Offline
Cost
Hot Start
< 4h offline
$100
Warm Start
4–8h offline
$400
Cold Start
≥8h offline
$900
Flat model charges $100 for everything
→ underprices cold starts by 9×
Wrong startup cost → wrong cycling decisions → wrong commitment → wrong LMPs
Notes: The cascade effect is key. The optimizer thinks cycling is cheap, so it cycles more than it should. That produces commitment decisions that real ISOs wouldn't make. And those wrong decisions flow through to wrong LMPs — which is exactly what we're trying to forecast accurately.

## Slide 5
Part 1 — Window-Based Binary Formulation
vs.
Window-Based Binary δ[g,s,t]
RHS = sum of existing binary switch_off vars
Always ≤ 1 → no Big-M needed
Tight LP bound → fast MILP solve
Two constraints per (generator, tier, period):
Σₛ δ[g,s,t] = v[g,t]
Exactly one tier chosen per startup event
δ[g,s,t] ≤ Σᵢ w[g,i] + pre_horizon
Unit was offline long enough to reach tier s
Bottom line: No Big-M constant needed — RHS is always ≤ 1, the LP relaxation stays tight, and branch-and-bound needs 3–10× fewer nodes than the countdown-timer approach.
Big-M Countdown Timer
Requires large constant M to encode
“if offline ≥ T hours”
Weakens LP relaxation → 3–10× more B&B nodes
Notes: The LP relaxation quality is the single most important factor in MILP solve time. Big-M formulations weaken it because the solver can't tell whether the integer constraint is nearly tight or very loose. In the window formulation, the RHS is a sum of binary variables — always between 0 and 1 — so the relaxation is as tight as possible without explicit branching.
When solving a MILP, the solver relaxes integer constraints to get a lower bound. Tight bounds yield shallow search trees (fast); loose bounds create deep trees requiring millions of node explorations. Big-M formulations produce loose bounds by making constraints artificially slack.

## Slide 6
Part 2 — N-1 Security at Scale
14,592
new inequalities if added upfront
(3× model size)
f_post[k,c,t] = f_k[t] + LODF[k,c] × f_c[t]
Post-contingency flow via pre-computed LODF matrix
Monitored branches
38
Contingencies
8
Time periods
24
Total inequalities
14,592
Notes: N-1 security is non-negotiable — it's a regulatory requirement in every major North American market. But the scale is the challenge: 39 total branches, 8 contingencies, 38 monitored per contingency, 24 periods, 2 directions — equals 14,592 inequalities before we even start branching. The question is how to handle that efficiently.

## Slide 7
Part 2 — Iterative Cutting-Plane
Key insight: fewer than 10% of N-1 constraints are binding at optimality.
1
Solve base SCUC (no N-1 constraints)
2
Compute f_post = f_k + LODF[k,c] × f_c for all contingencies
3
Find violated constraints: |f_post| > emergency_limit + ε
4
If none → STOP — solution is N-1 feasible
5
Add only the violated cuts → return to step 1
Measured — 24-Bus Main Case
2 iterations (converged)
32 constraints added
of 14,592 possible → 0.22%
Same optimal cost (±$1 vs. full)
+$7,941 N-1 security premium
Notes: These are the actual measured numbers from our 24-bus run. Only 32 of 14,592 possible N-1 constraints were violated by the base solution — that's 0.22%. We converged in exactly 2 iterations. The N-1 security premium is $7,941, or 1.2% above the base cost. The algorithm is provably correct: at convergence, every post-contingency flow has been checked numerically against its emergency limit.

## Slide 8
Part 3 — LMP Extraction via Fix-and-Re-Solve
Why not extract from MILP?
LP duality theory: every constraint has a shadow price
These shadow prices = LMPs
BUT: integer variables break LP duality
MILP solvers don't compute meaningful duals
Why this works
The fixed values were feasible in the original MILP — locking them can't violate any constraints, only remove degrees of freedom. The resulting LP is continuous throughout, so LP duality applies. The dual variables are well-defined and correctly interpreted as LMPs.
Fix-and-Re-Solve
1. Solve MILP (Parts 1 + 2) → optimal binary values
2. Lock all binaries: LB = UB = optimal value
3. Re-solve as pure LP (continuous dispatch only)
4. Extract duals → LMP[n,t] =−dual(nodal_balance[n,t])
Bottom line: Integer variables block LP duality — MILP shadow prices are meaningless. Fixing the optimal binaries converts the problem to a pure LP, restoring correct duals: the same LMPs an ISO would compute.
Notes: The fix-and-re-solve approach is the industry standard for LMP computation. You solve the unit commitment (with integer decisions), then lock those decisions and re-solve the economic dispatch as a pure LP to compute prices. This is exactly what ISOs do in practice — commitment is one solve, pricing is a separate solve.

## Slide 9
Part 3 — Six Actionable Trading Signals
1
Battery arbitrage (13.64× temporal)
Charge $2/MWh (h1–7) → discharge $28–37/MWh (h13–18). Expected spread $26–29/MWh per cycle.
2
Geographic arbitrage (north-south FTR)
B22 (renewables, $6.47) → B3 (thermal, $23.72) = $17.25/MWh structural spread.
3
Ramp spike opportunities
Hours 18 & 23 spike to $37.10 & $35.49 — caused by ramping, not load. Virtual bid can capture value.
4
Renewable hedging
Long renewable positions lose value in off-peak hours (1–7: only $7.56/MWh). Pair with peak-hour forward sales or storage.
5
Security-driven dispatch premium
N-1 tight hours (17–22): peaker commits for grid safety. Focus on congestion/FTR opportunities and avoid unhedged long energy positions.
6
Generator availability volatility
THERM_009 ($23.2/MWh) sets peak price. Outage → $3/MWh jump. Structure option positions around key generator risk.
Notes: These six signals come directly from the SCUC output and LMP analysis. Each one represents a concrete position or trade a fund could take. The signals are ranked by tractability: battery arbitrage is most liquid, generator availability volatility is most nuanced but potentially highest-alpha.

## Slide 10
Part 3 — What the Simulator Tells a Trader
Merit order deviation → constraint identification.
  When expensive generators run out-of-merit, transmission or security is binding. THERM_002 ($97.9/MWh) at hour 18 signals N-1 constraint, not load scarcity.
Congested line hours/magnitude → FTR targets.
  N-1 violations on specific (line, hour) pairs = premium for congestion-hedging FTRs. Hours 17–22 see tightest constraints.
LMP classification by regime.
  Off-peak ($2.11/MWh) vs. peak ($28.77/MWh) vs. high-ren ($7.56/MWh) — different regimes require different hedges.
Spatial LMP spreads → arbitrage sizing.
  B22 (renewables, $6.47) → B3 (thermal, $23.72) = $17.25/MWh structural spread. FTR economics: 100 MW × $17.25 × 24 × 365 = $15.1M/year.
Renewable suppression risk.
  Cheap local renewable output may be curtailed; LMP spread overstates true arbitrage. Risk collapses if transmission added or demand grows.
Result: $18.24 avg LMP | $17.25 spatial (B22→B3) | 13.64× peak/off-peak | High-ren $7.56/MWh
Notes: These five analytical techniques form the framework for interpreting SCUC output. They answer: what does deviation from merit order tell us? Which constraints matter most? How do we classify trading opportunity by time-of-day? What’s the real arbitrage size? What’s the risk? Each feeds into the next to build a complete picture.

## Slide 11
Clean, Layered Architecture
instance.json
24-bus, 24h, 39 lines
read.py
ScucInstance
build.py
Pyomo model
solution.py
solution.json
_add_startup_tier_costs()
← NEW: Part 1
solve_with_n1_cuts()
← NEW: Part 2
market_analysis.py
← NEW: Part 3
Part 1 — Startup tiers
Part 2 — N-1 cuts loop
Part 3 — Market analysis
Notes: The architecture is deliberately layered — read, build, solve, extract, analyze. Each layer has one job and is independently testable. The three new components drop cleanly into the existing pipeline without changing any interfaces. Part 1 lives inside the thermal block builder. Part 2 wraps the solve call. Part 3 is a pure post-processing step on the solution.

## Slide 12
Rigorous Test Coverage — 22 Tests, All Passing
Part 1 · test_startup_tiers.py (13 tests)
No δ variable for single-tier model (structural)
Correct variable count for multi-tier
Σ δ[g,s,t] = v[g,t] at optimality (algebraic)
Pre-horizon hot / warm / cold tier selection
Boundary: exactly Tᵊs hours offline → correct tier
In-horizon hot start (switch-off within window)
Equal delays → that tier is always zero
Economic: warm = hot + $300 exactly
Economic: cold = warm + $500 exactly
Part 2 · test_n1_security.py (9 tests)
n1_overflow keyset matches expected shape
Cut list empty before first solve
LODF matrix shape: (n_branches × n_branches)
Convergence within max_iter
Stats dict fully populated; last iter = 0 violations
Constraints added ≤ max possible
Post-solve N-1 feasibility verified numerically
Cutting-plane cost = full model cost (±$1)
Cutting-plane adds strictly fewer constraints than full model
Notes: I want to highlight the last N-1 test — the equivalence check between cutting-plane and full model. This is more than a unit test: it's a correctness proof. If they produce the same objective, we know the cutting-plane hasn't approximated anything. That's an important property to be able to demonstrate to a quant team.

## Slide 13
Conclusion
Three simulator upgrades — each targeting a specific pricing distortion.
Part 1 — Startup costs corrected. Cold restart were under priced by the flat model. Corrected cost: $649,871 total, 10/24 units committed.
Part 2 — N-1 security, efficiently. 14,592 possible constraints → 32 added in 2 iterations (0.22%). Full N-1 feasibility at $657,811 — a $7,941 security premium.
Part 3 — Correct LMPs extracted. Fix-and-re-solve restores LP duality: $18.24 avg LMP, 13.64× peak/off-peak ratio, $17.25/MWh north–south spread — six actionable trading signals.
The simulator now produces prices grounded in real grid economics — a credible foundation for LMP forecasting and trading alpha.

## Slide 14
Delivered
✓
Part 1: Tiered startup costs — $649,871 total cost, 10/24 units, ISO-standard formulation
✓
Part 2: N-1 security — $657,811 (+$7,941), 2 iterations, 32 cuts of 14,592 (0.22%)
✓
Part 3: Market analysis — $18.24 avg LMP, 13.64× peak/off-peak, $17.25 spatial spread (B22→B3)
✓
22 unit tests — all passing: structural, algebraic, economic, N-1 feasibility
✓
Clean pipeline: read → build → solve → analyze → trade
Questions?
Notes: To close: all three parts are implemented, tested, and the numbers are in. Part 1: $649,871, no unnecessary cycling. Part 2: N-1 secure for $7,941 more, achieved in 2 iterations adding only 32 constraints — 0.22% of what the full model would require. Part 3: $18.24 average LMP, 13.64× temporal spread, $17.25 spatial spread — clear storage and FTR signals. I'm happy to go deep on any of this — the formulation math, the convergence proof, the test design, or the market analysis interpretation. What questions do you have?